## Slide 1: Module 2: Basic Switch and End Device Configuration
Instructor Materials
Introduction to Networks v7.0 (ITN)
Notes: Cisco Networking Academy Program
CCNA 1
Module 2: Basic Switch and End Device Configuration

## Slide 2: Instructor Materials – Module 2 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the module
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide #13
  Note: Remove the Planning Guide from this presentation before sharing with anyone.
For additional help and resources go to the Instructor Home Page and Course Resources for this course. You also can visit the professional development site on netacad.com, the official Cisco Networking Academy Facebook page, or Instructor Only FB group.
Notes: 2

## Slide 3: What to Expect in this Module
To facilitate learning, the following features within the GUI may be included in this module:
Feature | Description
Animations | Expose learners to new skills and concepts.
Videos | Expose learners to new skills and concepts.
Check Your Understanding(CYU) | Per topic online quiz to help learners gauge content understanding.
Interactive Activities | A variety of formats to help learners gauge content understanding.
Syntax Checker | Small simulations that expose learners to Cisco command line to practice configuration skills.
PT Activity | Simulation and modeling activities designed to explore, acquire, reinforce, and expand skills.

## Slide 4: What to Expect in this Module (Cont.)
Feature | Description
Hands-On Labs | Labs designed for working with physical equipment.
Class Activities | These are found on the Instructor Resources page. Class Activities are designed to facilitate learning, class discussion, and collaboration.
Module Quizzes | Self-assessments that integrate concepts and skills learned throughout the series of topics presented in the module.
Module Summary | Briefly recaps module content.
To facilitate learning, the following features may be included in this module:

## Slide 5: Check Your Understanding
Check Your Understanding activities are designed to let students quickly determine if they understand the content and can proceed, or if they need to review.
Check Your Understanding activities do not affect student grades.
There are no separate slides for these activities in the PPT. They are listed in the notes area of the slide that appears before these activities.
Notes: 5

## Slide 6: Module 2: Activities
What activities are associated with this module?
Page # | Activity Type | Activity Name | Optional?
2.1.6 | Check Your Understanding | Cisco IOS Access | Recommended
2.2.3 | Video | IOS CLI Primary Command Modes | Recommended
2.2.5 | Video | Navigate Between IOS Modes | Recommended
2.2.7 | Syntax Checker | Navigate Between IOS Modes | Recommended
2.2.8 | Check Your Understanding | IOS Navigation | Recommended
2.3.4 | Video | Context Sensitive Help and Command Syntax Check | Recommended
2.3.6 | Video | Hot Keys and Shortcuts | Recommended
2.3.7 | Packet Tracer | Navigate the IOS | Recommended
Notes: 6

## Slide 7: Module 2: Activities (Cont.)
What activities are associated with this module?
Page # | Activity Type | Activity Name | Optional?
2.3.8 | Lab | Navigate the IOS by Using Tera Term for Console Connectivity | Recommended
2.4.6 | Video | Secure Administrative Access to a Switch | Recommended
2.4.7 | Syntax Checker | Basic Device Configuration | Recommended
2.4.8 | Check Your Understanding | Basic Device Configuration | Recommended
2.5.3 | Video | Alter the Running Configuration | Recommended
2.5.5 | Packet Tracer | Configure Initial Switch Settings | Recommended
2.6.3 | Check Your Understanding | Ports and Addresses | Recommended
2.7.3 | Syntax Checker | Verify Windows PC IP Configuration | Recommended
Notes: 7

## Slide 8: Module 2: Activities (Cont.)
What activities are associated with this module?
Page # | Activity Type | Activity Name | Optional?
2.7.5 | Syntax Checker | Configure a Switch Virtual Interface | Recommended
2.7.6 | Packet Tracer | Implement Basic Connectivity | Recommended
2.8.1 | Video | Test the Interface Assignment | Recommended
2.8.2 | Video | Test End-to-End Connectivity | Recommended
2.9.1 | Packet Tracer | Basic Switch and End Device Configuration | Recommended
2.9.2 | Lab | Basic Switch and End Device Configuration | Recommended
Notes: 8

## Slide 9: Module 2: Best Practices
Prior to teaching Module 2, the instructor should:
Review the activities and assessments for this module.
Try to include as many questions as possible to keep students engaged during classroom presentation.
Topic 2.1
  Ask the students or have a class discussion
    What are the advantages and disadvantages of using a GUI interface or CLI?
    Why is SSH more important to use instead of Telnet?
    If available, show the class how to remotely access a switch by using a terminal emulation program such as Tera Term or PuTTY.
Notes: 9

## Slide 10: Module 2: Best Practices (Cont.)
Topic 2.2
  Ask the students or have a class discussion
    Explain the differences between User EXEC mode and Privileged EXEC mode. You can write the switch prompts on the board and explain the prompts will display the current mode.
    Why do you think the commands available in User EXEC mode are limited?
    What are the differences between Privilege EXEC mode and Global Configuration mode?
    Draw the different IOS mode prompts on the board and explain the differences between the configuration modes and how to tell which mode the switch is currently in.
Topic 2.3
  Ask the students or have a class discussion
    Draw the basic IOS command structure on the board and describe the syntax
    What hot keys or shortcuts do you use on your computers? (F5 to refresh, Ctrl+C to copy, Ctrl+S to save etc.)
    If possible, display the CLI of a switch and show the help feature for various commands.
Notes: 10

## Slide 11: Module 2: Best Practices (Cont.)
Topic 2.4
  Ask the students or have a class discussion
    Explain the guidelines for naming a network device and why the default name should be changed.
    Why would you want to encrypt all the passwords on a switch?
    Why is a banner important to configure on a network device?
Topic 2.5
  Ask the students or have a class discussion
    What would be a disadvantage of reloading a switch?
    What is the difference between the running-config and the startup-config?
    If possible, walkthrough an example of capturing the running-config or startup-config to a text file.
Notes: 11

## Slide 12: Module 2: Best Practices (Cont.)
Topic 2.6
  Ask the students or have a class discussion
    Name some end devices that are configured with IP addresses. Why do they need to be configured with an IP address?
    If available, show various network media such as Ethernet cables or fiber-optic cables and how they connect to a port on the switch.
Topic 2.7
  Ask the students or have a class discussion
    Have you ever configured your computer with a manual IP address?
    Why do you need to use the no shutdown command on an interface?
Topic 2.8
  Ask the students or have a class discussion
    Why is it important to test end-to-end connectivity?
Notes: 12

## Slide 13: Module 2: Basic Switch and End Device Configuration
Introductions to Networks v7.0 (ITN)
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0
Module 2: Basic Switch and End Device Configuration

## Slide 14: Module Objectives
  Module Title: Basic Switch and End Device Configuration
  Module Objective: Implement initial settings including passwords, IP addressing, and default gateway parameters on a network switch and end devices.
Topic Title | Topic Objective
Cisco IOS Access | Explain how to access a Cisco IOS device for configuration purposes.
IOS Navigation | Explain how to navigate Cisco IOS to configure network devices.
The Command Structure | Describe the command structure of Cisco IOS software.
Basic Device Configuration | Configure a Cisco IOS device using CLI.
Save Configurations | Use IOS commands to save the running configuration.
Ports and Addresses | Explain how devices communicate across network media.
Configure IP Addressing | Configure a host device with an IP address.
Verify Connectivity | Verify connectivity between two end devices.
Notes: 14
2 – Basic Switch and End Device Configuration
2.0.2 – What will I learn to do in the module?

## Slide 15: 2.1 Cisco IOS Access
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access

## Slide 16: Cisco IOS Access Operating Systems
Shell - The user interface that allows users to request specific tasks from the computer. These requests can be made either through the CLI or GUI interfaces.
Kernel - Communicates between the hardware and software of a computer and manages how hardware resources are used to meet software requirements.
Hardware - The physical part of a computer including underlying electronics.
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.1 – Operating Systems

## Slide 17: Cisco IOS Access GUI
A GUI allows the user to interact with the system using an environment of graphical icons, menus, and windows.
A GUI is more user-friendly and requires less knowledge of the underlying command structure that controls the system.
Examples of these are: Windows, macOS, Linux KDE, Apple iOS and Android.
GUIs can fail, crash, or simply not operate as specified. For these reasons, network devices are typically accessed through a CLI.
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.2 – GUI

## Slide 18: Cisco IOS Access Purpose of an OS
PC operating system enables a user to do the following:
  Use a mouse to make selections and run programs
  Enter text and text-based commands
  View output on a monitor
CLI-based network operating system enables a network technician to do the following:
  Use a keyboard to run CLI-based network programs
  Use a keyboard to enter text and text-based commands
  View output on a monitor
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.3 – Purpose of an OS

## Slide 19: Cisco IOS Access Access Methods
Console – A physical management port used to access a device in order to provide maintenance, such as performing the initial configurations.
Secure Shell (SSH) – Establishes a secure remote CLI connection to a device, through a virtual interface, over a network. (Note: This is the recommended method for remotely connecting to a device.)
Telnet – Establishes an insecure remote CLI connection to a device over the network. (Note: User authentication, passwords and commands are sent over the network in plaintext.)
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.4 – Access Methods

## Slide 20: Cisco IOS Access Terminal Emulation Programs
Terminal emulation programs are used to connect to a network device by either a console port or by an SSH/Telnet connection.
There are several terminal emulation programs to chose from such as PuTTY, Tera Term and SecureCRT.
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.5 – Terminal Emulation Programs
2.1.6 – Check Your Understanding - Cisco IOS Access

## Slide 21: 2.2 IOS Navigation
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation

## Slide 22: IOS Navigation Primary Command Modes
User EXEC Mode:
  Allows access to only a limited number of basic monitoring commands
  Identified by the CLI prompt that ends with the > symbol
Privileged EXEC Mode:
  Allows access to all commands and features
  Identified by the CLI prompt that ends with the # symbol
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.1 – Primary Command Modes

## Slide 23: IOS Navigation Configuration Mode and Subconfiguration Modes
Global Configuration Mode:
  Used to access configuration options on the device
Line Configuration Mode:
  Used to configure console, SSH, Telnet or AUX access
Interface Configuration Mode:
  Used to configure a switch port or router interface
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.2 – Configuration Mode and Subconfiguration Modes

## Slide 24: IOS Navigation Video – IOS CLI Primary Command Modes
This video will cover the following:
  User EXEC mode
  Privilege EXEC mode
  Global Config mode
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.3 – Video - IOS CLI Primary Command Modes

## Slide 25: IOS Navigation Navigation Between IOS Modes
Privileged EXEC Mode:
  To move from user EXEC mode to privilege EXEC mode, use the enabled command.
Global Configuration Mode:
  To move in and out of global configuration mode, use the configure terminal command. To return to privilege EXEC mode, use the exit command.
Line Configuration Mode:
  To move in and out of line configuration mode, use the line command followed by the management line type. To return to global configuration mode, use the exit command.
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 26: IOS Navigation Navigation Between IOS Modes (Cont.)
Subconfiguration Modes:
  To move out of any subconfiguration mode to get back to global configuration mode, use the exit command. To return to privilege EXEC mode, use the end command or key combination Ctrl +Z.
  To move directly from one subconfiguration mode to another, type in the desired subconfiguration mode command. In the example, the command prompt changes from (config-line)# to (config-if)#.
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 27: IOS Navigation Video – Navigation Between IOS Modes
This video will cover the following:
  enable
  disable
  configure terminal
  exit
  end
  Control + Z on keyboard
  Other commands to enter sub configuration modes
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.5 – Video - Navigate Between IOS Modes
2.2.6 – A Note About Syntax Checker
2.2.7 – Syntax Checker – Navigate Between IOS Modes
2.2.8 – Check Your Understanding - IOS Navigation

## Slide 28: 2.3 The Command Structure
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure

## Slide 29: The Command Structure Basic IOS Command Structure
Keyword – This is a specific parameter defined in the operating system (in the figure, ip protocols).
Argument - This is not predefined; it is a value or variable defined by the user (in the figure, 192.168.10.5).
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.1 – Basic IOS Command Structure

## Slide 30: The Command Structure IOS Command Syntax Check
A command might require one or more arguments. To determine the keywords and arguments required for a command, refer to the command syntax.
  Boldface text indicates commands and keywords that are entered as shown.
  Italic text indicates an argument for which the user provides the value.
Convention | Description
boldface | Boldface text indicates commands and keywords that you enter literally as shown.
italics | Italic text indicates arguments for which you supply values.
[x] | Square brackets indicate an optional element (keyword or argument).
{x} | Braces indicate a required element (keyword or argument).
[x {y ¦ z }] | Braces and vertical lines within square brackets indicate a required choice within an optional element. Spaces are used to clearly delineate parts of the command.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.2 – IOS Command Syntax Check

## Slide 31: The Command Structure IOS Command Syntax Check (Cont.)
The command syntax provides the pattern, or format, that must be used when entering a command.
The command is ping and the user-defined argument is the ip-address of the destination device. For example, ping 10.10.10.5.
The command is traceroute and the user-defined argument is the ip-address of the destination device. For example, traceroute 192.168.254.254.
If a command is complex with multiple arguments, you may see it represented like this:
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.2 – IOS Command Syntax Check

## Slide 32: The Command Structure IOS Help Features
The IOS has two forms of help available: context-sensitive help and command syntax check.
Context-sensitive help enables you to quickly find answers to these questions:
    Which commands are available in each command mode?
    Which commands start with specific characters or group of characters?
    Which arguments and keywords are available to particular commands?
Command syntax check verifies that a valid command was entered by the user.
    If the interpreter cannot understand the command being entered, it will provide feedback describing what is wrong with the command.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.3 – IOS Help Features

## Slide 33: The Command Structure Video – Context Sensitive Help and Command Syntax Checker
This video will cover the following:
  Use the help command in user EXEC, privileged EXEC, and global config mode
  Finish commands and arguments with the help command
  Use the command syntax checker to fix syntax errors and incomplete commands
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.4 – Video - Context Sensitive Help and Command Syntax Checker

## Slide 34: The Command Structure Hot Keys and Shortcuts
The IOS CLI provides hot keys and shortcuts that make configuring, monitoring, and troubleshooting easier.
Commands and keywords can be shortened to the minimum number of characters that identify a unique selection. For example, the configure command can be shortened to conf because configure is the only command that begins with conf.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.5 – Hot Keys and Shortcuts

## Slide 35: The Command Structure Hot Keys and Shortcuts (Cont.)
The table below is a brief list of keystrokes to enhance command line editing.
Keystroke | Description
Tab | Completes a partial command name entry.
Backspace | Erases the character to the left of the cursor.
Left Arrow or Ctrl+B | Moves the cursor one character to the left.
Right Arrow or Ctrl+F | Moves the cursor one character to the right.
Up Arrow or Ctrl+P | Recalls the commands in the history buffer, beginning with the most recent commands.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.5 – Hot Keys and Shortcuts

## Slide 36: The Command Structure Hot Keys and Shortcuts (Cont.)
When a command output produces more text than can be displayed in a terminal window, the IOS will display a “--More--” prompt. The table below describes the keystrokes that can be used when this prompt is displayed.
The table below lists commands that can be used to exit out of an operation.
Note: To see more hot keys and shortcuts refer to 2.3.5.
Keystroke | Description
Ctrl-C | When in any configuration mode, ends the configuration mode and returns to privileged EXEC mode.
Ctrl-Z | When in any configuration mode, ends the configuration mode and returns to privileged EXEC mode.
Ctrl-Shift-6 | All-purpose break sequence used to abort DNS lookups, traceroutes, pings, etc.
Keystroke | Description
Enter Key | Displays the next line.
Space Bar | Displays the next screen.
Any other key | Ends the display string, returning to privileged EXEC mode.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.5 – Hot Keys and Shortcuts

## Slide 37: The Command Structure Video – Hot Keys and Shortcuts
This video will cover the following:
  Tab key (tab completion)
  Command shortening
  Up and down arrow key
  CTRL + C
  CTRL + Z
  CTRL + Shift + 6
  CTRL + R
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.6 – Video - Hot Keys and Shortcuts

## Slide 38: The Command Structure Packet Tracer – Navigate the IOS
In this Packet Tracer, you will do the following:
Establish Basic Connections, Access the CLI, and Explore Help
Explore EXEC Modes
Set the Clock
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.7 – Packet Tracer – Navigate the IOS

## Slide 39: The Command Structure Lab – Navigate the IOS by Using Tera Term for Console Connectivity
In this lab, you complete the following objectives:
Access a Cisco Switch through the Serial Console Port
Display and Configure Basic Device Settings
(Optional) Access a Cisco Router Using a Mini-USB Console Cable
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.8 – Lab – Navigate the IOS by Using Tera Term for Console Connectivity